## Slide 1: Weekly meeting 09/09/22
By: Jeremy Benik

## Slide 2: Last week to do
Read paper about Rothermel
  Working on balbi PowerPoint then I will read this
Write report on pressure sensors
  In progress
Add SODAR Data to the sounding
  completed
Get final ff2 simulation
  Done, currently running
Compute ROS with Rothermel model
  In progress
Compute ROS with Balbi model (once that’s implemented)
Make powerpoint about Balbi paper
  In progress
Play with w_0 in balbi model
  Run a case and change that and see what we get
  Done

## Slide 3: Adding sodar data to sounding
To add the SODAR data to the sounding, I created a plot of the potential temperature and mixing ratio from 20m to 260m
With this plot I linearly fit the missing values
With these values, I input them into the input_sounding file
To decrease the upper level wind speeds, I decreased the upper level winds by 1m/s (accounting for direction)
I used matlab for this process as zooming in graphs is much easier on that platform

## Slide 4: Adding sodar data to sounding

## Slide 5: New sim with SODAR data

## Slide 6: Smoothing out sodar data
In the input_sounding, the SODAR data had a few rough spots where the wind speeds changed rapidly with height

## Slide 7: Simulation with modified sodar data
With the new smoothed out SODAR data, I ran another simulation and this simulation is by far the best simulation we currently have
We noticed 600 seconds into the simulation may be a point to start the run, so the namelist.input was adjusted (along with the ignition times) to change the initialization to 600 seconds instead of 1200

## Slide 8: Simulation with modified sodar data

## Slide 9: Balbi w_0 sensitivity
After looking through the code and meeting with John and Dr. Kochanski, the w_0 can not be omitted and assumed to be 50
This mainly applies to ideal simulations with a small ignition line in the beginning as larger fires will likely have too large of an ignition line
The graph shows there’s a linear fit for w_0 which comes as a surprise since there is an exponential in the r_c equation
Testing was done on the matlab balbi code (2021 update) with varying w_0 to see how much it change the ROS

## Slide 10: Balbi w_0 sensitivity
Chart: Sensitivity Analysis of W_0
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35 | 36 | 37 | 38 | 39 | 40 | 41 | 42 | 43 | 44 | 45 | 46 | 47 | 48 | 49 | 50 | 51 | 52 | 53 | 54 | 55 | 56 | 57 | 58 | 59 | 60
ros | 0.0553 | 0.0594 | 0.0634 | 0.0674 | 0.0714 | 0.0754 | 0.0793 | 0.0833 | 0.0872 | 0.0911 | 0.095 | 0.0989 | 0.1028 | 0.1067 | 0.1105 | 0.1144 | 0.1182 | 0.1221 | 0.1259 | 0.1297 | 0.1335 | 0.1373 | 0.1411 | 0.1449 | 0.1487 | 0.1525 | 0.1563 | 0.1601 | 0.1638 | 0.1676 | 0.1713 | 0.1751 | 0.1788 | 0.1826 | 0.1863 | 0.1901 | 0.1938 | 0.1975 | 0.2013 | 0.205 | 0.2087 | 0.2124 | 0.2161 | 0.2199 | 0.2236 | 0.2273 | 0.231 | 0.2347 | 0.2384 | 0.2421 | 0.2421 | 0.2421 | 0.2421 | 0.2421 | 0.2421 | 0.2421 | 0.2421 | 0.2421 | 0.2421 | 0.2421
R_c | 0.0036 | 0.0071 | 0.0107 | 0.0143 | 0.0179 | 0.0215 | 0.025 | 0.0286 | 0.0322 | 0.0358 | 0.0393 | 0.0429 | 0.0465 | 0.0501 | 0.0536 | 0.0572 | 0.0608 | 0.0644 | 0.0679 | 0.0715 | 0.0751 | 0.0787 | 0.0823 | 0.0858 | 0.0894 | 0.093 | 0.0966 | 0.1001 | 0.1037 | 0.1073 | 0.1109 | 0.1144 | 0.118 | 0.1216 | 0.1252 | 0.1288 | 0.1323 | 0.1359 | 0.1395 | 0.1431 | 0.1466 | 0.1502 | 0.1538 | 0.1574 | 0.1609 | 0.1645 | 0.1681 | 0.1717 | 0.1753 | 0.1788 | 0.1788 | 0.1788 | 0.1788 | 0.1788 | 0.1788 | 0.1788 | 0.1788 | 0.1788 | 0.1788 | 0.1788
R_f | 0.0089 | 0.0094 | 0.0098 | 0.0103 | 0.0107 | 0.0111 | 0.0114 | 0.0118 | 0.0122 | 0.0125 | 0.0128 | 0.0131 | 0.0134 | 0.0137 | 0.014 | 0.0143 | 0.0146 | 0.0148 | 0.0151 | 0.0153 | 0.0156 | 0.0158 | 0.016 | 0.0162 | 0.0165 | 0.0167 | 0.0169 | 0.0171 | 0.0172 | 0.0174 | 0.0176 | 0.0178 | 0.018 | 0.0181 | 0.0183 | 0.0185 | 0.0186 | 0.0188 | 0.0189 | 0.0191 | 0.0192 | 0.0194 | 0.0195 | 0.0196 | 0.0198 | 0.0199 | 0.02 | 0.0201 | 0.0203 | 0.0204 | 0.0204 | 0.0204 | 0.0204 | 0.0204 | 0.0204 | 0.0204 | 0.0204 | 0.0204 | 0.0204 | 0.0204

## Slide 11: Final ff2 simulation
Currently on Cheyenne, I’m running the final FF2 simulation
  Over the past few months, tests have been run on a modified version of the FF2 simulation to match initial conditions between the simulation and observations
  Since this run is at 5m, it takes much longer to run, so the run is currently being done on Cheyenne at: /glade/scratch/jbenik/FF2_Final_Sim_09_08_22

## Slide 12: to do
Read paper about Rothermel
  Working on balbi PowerPoint then I will read this
Write report on pressure sensors
  In progress
Compute ROS with Rothermel model
  In progress
Compute ROS with Balbi model (once that’s implemented)
Make powerpoint about Balbi paper
  In progress
Create the surface plot for balbi with 3 dimensions