## Slide 1: Rothermel model
By: Jeremy Benik

## Slide 2: abstract
Adjustments were made by Frank A. Albini in 1976
It has been used in fire and fuels management systems since 1972

## Slide 3: intro
The Rothermel model is the most commonly used model in the U.S. fire management systems, with a lot of use outside USA
Physics models attempts to represent both the physics and chemistry of fire spread, quasi-physical model attempts to represent only the physics, empirical model is one that contains no physical basis at all and is generally statistical in nature, and quasi-empirical is one that uses some form of physical framework on which the statistical modeling is based
Rothermel’s model is categorized as quasi-empirical
  It is based on a heat balance model developed by Frandsen(1971), data from wind tunnel experiments in artificial fuel beds of varying characteristics (rothermel and Anderson 1966), and Australian wildfire data in grasses (McArthur 1969)

## Slide 4: intro
The basic Rothermel model with some minor modifications by albini has been used in the same form for decades
The model is based on the conservation of energy described by a heat sink (Fransden 1971)
It assumes a linear flame front and calculates spread rate of a head fire with or without wind or slope
The model is meant for fire burning through uniform fuel (both live and dead)
This model only addresses fire in surface fuel, does not work in crown fires, smoldering ground fires, or post-frontal combustion of fuels
It’s strengths are simplicity of input requirements and calculations and the possibility of changing many driving variables such as fuel

## Slide 5: Development and application
The lab was in the Missoula fire science laboratory, dedicated in the 1960s which had a combustion lab and two wind tunnels where researchers could xamine the rate of spread under various conditions
Rothermel and Anferson were brought in from Chief Jack Barrows who recognized there is a need for understanding the basics of fire behaviour and he wanted a physical scientists and engineer
Took 10 years to produce a fire behaviour model, and 10 more years to learn how to obtain the inputs and interpret the outputs for use by the “man on the ground”
Experimental burning was done in fuel beds of a single size class

## Slide 6: Section 3 the surface fire spread model
The Rothermel model is based on a foundation provided by Fransden (1971) who applied the conservation of energy to a unit volume of fuel ahead of a steadily advancing fire in a homogeneous fuel bed
Changes from the Rothermel model from Albini
  Correction for mineral content
  Mineral damping coefficient
  Reaction velocity correlation
  Weighting factors for fuel load
  Moisture of extinction of live fuels
  Weighting factor on intensity by category