## Slide 1: Extension of the Balbi fire spread model to include the field scale conditions of shrubland fires
By: Jeremy Benik

## Slide 2: Goal of balbi model
The goal of the balbi model is to provide a “simplified rate of spread model aimed at providing computationally fast and accurate simulations of fire propagation that can be used by fire managers under operational conditions” (Balbi 2022, abstract)
This version accounts for both radiation and convective heat transfer
The difference between this paper and the 2021 paper is this accounts for outdoor fires rather than just laboratory fires
This model remains “physics-based and is faster than real time and fully predictive” (Balbi 2022, abstract)

## Slide 3: History of the balbi model
The first balbi model was presented in 2007 and followed the assumptions that radiation was the main heat transfer mode
With the next two versions of the mode, there were improvements in the physical basis of the model
  Incorporating the euation for vertical momentum applied to the flame and introduction of a fresh cooling air provided better modeling of the radiative fraction
Then Chatelon developed a convective model for well ordered and vertically oriented fuel beds

## Slide 4: Model idealisation
Some of the 2020 concepts were kept
Some assumptions kept are
  Fresh airstream enters the flame base
  Hot gasses from the upper layer are driven to the top of the flame base and create the free flame structure above the vegetal stratum
  Mixed air pyrolysis gases from the lower layer go out through the front panel of the fuel-burning particles area and create an internal, or combustion zone, flame that directly contacts the unburnt fuel
4 energy contributions suggested by Balbi in 2020 are kept
  Flame base radiation, flame radiation, convective cooling, convective heating

## Slide 5: Main equation
R = R_b + R_c + R_r

## Slide 6: Changes from lab
In eq6, the factor 2 is removed since it is assumed that at a field scale the soil absorbs a part of the flame base radiative flux
The optical depth is inversely proportional to the fuel porosity
The leaf areas ratio is added to the scaling factor a_b since the heat release affects the live fuel and spread of ignition mainly depends on the catalytic effect of dead fuel
Combustion of live fuelsdoes not directly contribute to movement of the ignition interface and so does not create the fire dynamics but takes part in the flame base combustion anyway. Its contribution is added in the model as a ratio between dead and total packing ratio

## Slide 7: A_r & a_c
This is related to the flame radiation heat flux
Only the absorption of this heat flux by the unburnt fuel is concerned
A_c is related to the convective heat flux is now in three contributions which are mostly energy losses
  These factors are the heat provided to the unburnt live fuel a_liv
  A_lat are heat losses on lateral edges of the fire front
    This depends on the fireline width w_0
  A_up amount of pyrolysis gases produced by the air stream below the streamline that enters the flame base at E
    The second part is the heat remaining in the fuel-burning particles when the hear is released to the upper part of the fuel is removed

## Slide 8: Iterative method
Since there are so many factors involved in calculating the ROS, this leads to a nonlinear algebraic equation, an iterative method is necessary to numerically solce this equation by using the first term as the solution (R_c) to then loop through and converge to a value

## Slide 9: data
To calibrate the model, shrublands in Turkey were used to estimate the a_m parameter (fitted model parameter)
Using this data (more mentioned in the paper), the am parameter was calculated
For a sensitivity analysis, different fuel parameters were tested on the model R, which allows an analysis of the most influential variables in the R output

## Slide 10: Testing the model
To benchmark the data, the model was compared to other models using the same dataset
Some of these models are old balbi models and the Anderson model

## Slide 11: Numerical results
A_m remains at 0.025
R increased linearly with wind speed for the lower fuel loads
For heavier fuel loads, slow increase in ROS with lower wind speeds, then past 2.5m/s there is a much steeper increase in ROS
With increasing fuel load, ROS increases
Fuel load, fuel height, bulk density are connected

## Slide 12: Numerical results
FMC on ROS

## Slide 13: Numerical results
Fuel bed height on ROS
ROS is found to increase with fuel height independent of the wind speed
A doubling of fuel height 1m to 2m increased ROS by 31% (more pronounced for low wind speeds)