## Slide 1: Adjustment Factors in WRF-sfire
By: Jeremy Benik

## Slide 2: ADjr0 adjustments in wrf-sfire
Initially, we wanted to match the backfire rate of spread in the simulation to the observed backfire rate of spread
To calculate the observed backfire rate of spread, I used videos of the burn and google earth to calculate the backfire rate of spread
A more in depth explanation of how this was calculated can be found on YouTube at: https://www.youtube.com/watch?v=nI3wS8YHofM
As an attempt to match the simulations to the observed backfire rate of spread, we added in an adjr0 adjustment factor to the namelist.fire to slow down the simulation
Example of the adjustment factors in the namelist.fire

## Slide 3: ADjr0 adjustments in wrf-sfire
The observed backfire ROS was about 0.02m/s, and the simulation was at 0.021 m/s
In an attempt to slow the simulation down, an adjustment factor was added to the simulation
  The adjustment factor used in the initial run is 0.90677
With this adjustment factor, we were expecting the backfire ROS to be closer to 0.02, but instead the new backfire ROS was calculated to be 0.015m/s
To try to better correct the model, another run was performed this time with a different adjustment factor of 0.93
This did increase the backfire ROS, but not as much as we had hoped
  The new backfire ROS was 0.016

## Slide 4: ADjr0 adjustments in wrf-sfire
We ran many more simulations to try to match the observed backfire ROS, but nothing was close
  With an adjr0 of 0.9999, that yielded a backfire ROS of 0.018m/s
After looking in the WRF-SFIRE, it appears that the adjr0 is multiplied over and over again in the code, meaning any small adjustment factor will be amplified

## Slide 5: How was the backfire ROS calculated?
To calculate the backfire ROS, I picked a time in simulation where all the initial ran to (about 900 seconds into the simulation)
Then I found a point where the fire_area had just touched the grid cell but had not fully engulfed it (fire_area < 1)
With this location, I calculated the distance to the point using the fxlat and fxlong location, and the location of the ignition point since that is specified on the grid
With the time and distance, I then calculated the backfire ROS

## Slide 6: results
run 1 Backfire ROS was 0.015989734039574453
run 2 Backfire ROS was 0.016798221788879665
run 3 Backfire ROS was 0.01709021600282394
run 4 Backfire ROS was 0.01720178385015444
run 5 Backfire ROS was 0.01767115575900313
run 6 Backfire ROS was 0.017712621441470035
run 7 Backfire ROS was 0.017739540319040657

## Slide 7: Adjustment factors in wrf-sfire
To further test the adjustment factors in WRF-SFIRE, I tested the adjustment factors on the small hill case
  This simulation was picked since it had a slope, and it was small enough to be able to run in a couple minutes
There were 21 simulations run
  1 simulation was done with no adjustment factors, and the other 20 had different adjustments factors applied in the namelist.fire
Example of one of the runs:

## Slide 8: Adjustment factors in wrf-sfire
To see how the rate of spread was impacted, I found three points along the burn plot
  Centre of the hill
  North East part of the hill
  South west part of the hill
With these points, I found where the fire_area was greater than 0 and the time this occurred
Then I found the wind speed at those points at the time the fire reached those points
To calculate the distance, I took the ignition point and found the distance from there to those locations

## Slide 9: Adjustment factors results
This excel sheet can be found on my github at: https://github.com/Jeremy-Benik/Hill_Runs/blob/main/ROS_calculations.xlsx
The Rothermel codes can be found at: https://github.com/Jeremy-Benik/Hill_Runs/blob/main/Codes/
The modified fuel code can be found at: https://github.com/Jeremy-Benik/Hill_Runs/blob/main/Codes/fuels.m

## Slide 10: Adjustment factors in wrf-sfire
For comparison, I have the ”original” Rothermel code (all that was changed is the model doesn’t max out at 6m/s) and the ROS variable from the model to see how the modified Rothermel model compares
  The modified Rothermel code takes the adjustment factors as an input, and is integrated in the code during the rate of spread calculation
  Please note: the columns that do not have any data are because the simulation never reached those locations on the burn plot